## Slide 1
Check Call
Cheat Codes
How do I set a check call?
Logistics

## Slide 2: Event
The ones that are tracking for OTD
Loads on Trucker Tools/ MP
Enroute to Pick up
Loading/Unloading
Action
2 hours prior to delivery if under 24 hours, or every 12 hours if delivery is over 24 hours
2 hours before pick up based on time zone
2 hours after current time
Communication
Escalation
No
No
No

## Slide 3: Event
The ones that involve late arrivals
Communication Escalation
Late for Pickup or Delivery - Same Day
Late for Pickup or Delivery - Future Date
Action
Now + 1 hour after current time and every 1 hour until resolved.
Now + 1 hour after current time and every 1 hour until resolved.
*Email CSR and AM with details
*Email CSR with details
Yes
Yes

## Slide 4: Event
The ones that involve Truck Issues
Communication
*Email CSR with details
Escalation
Breakdown
Overweight
Under Gross but Over on an Axle- Call shipper and advise truck needs to come back in to re-work, get confirmation they
will re-work it and document
Over Gross- *Email the CSR AND AM right away with details
Yes
Yes
Action
Now + 1 hour after current time and 1 hour until resolved
Action
Now +1 hour after current time and 1 hour until resolved
Get scale ticket (see where weight issue is, axle over gross) and BOL (verify correct product is loaded) right away
12,000 Steer Axle(tractor)
34,000 Drive Axle(trailer nose)
Get scale ticket (see whereweight issue is, axle orgross) and BOL (verify correctproduct is loaded) right away
12,000 Steer Axle(tractor)
34,000 Drive Axle(trailer nose)
34,000 Tandem Axle(trailer tail)
80,000 Gross

## Slide 5: Event
The ones that involve Delivery issues
Pickup or Delivery number not working
Action
Now +30 min or until resolved
Communication
Verify the number the driver is trying to use. See if any others in the pickup number or pickup time fields.
If new numbers provided work then no communication is needed.
If no additional numbers are available and nothing on hand is working email the CSR.
Escalation
No
No
Yes